## Slide 1: Grids and Direction

## Slide 2: Compass Rose ‘Anatomy’
Compass Roses have several divisions of direction (they are referred to as ‘points’).
  -Cardinal Points: the 4 main direction
  (North, East, South, West)
  -Ordinal Points: the 4 points between the cardinal points.
  (Northeast, South east, Southwest, Northwest)

## Slide 3
E
S
W
NE
SE
SW
NW

## Slide 4
NE
E
East North East
North North East
Half-winds: directions between Cardinal and Ordinal Points.
The North and South directions go before east and west (e.g. NNE, SSW), except when there are two Easts or Wests, in which case North and South are placed in the middle (e.g. ENE, WSW)

## Slide 5: More Divisions…
  Half-winds: 8 divisions of the cardinal and ordinal points.
  e.g. NNE, ENE, ESE, SSE,
  SSW, WSW, WNW, NNW
  Quarter-winds: 16 further divisions
  There is, however, an even more specific method of indicating direction.
  What might this method be?

## Slide 6: Degrees
For more specific direction, the compass is divided into 360 degrees.
North corresponds to 0 and 360.
South corresponds to 180.
When you use a compass, the compass BEARING is the direction in degrees that you need to go.
e.g. If you are going East South East, your compass bearing would be:
If you are going West North West, your compass bearing would be:
112.5 degrees
292.5 degrees

## Slide 7: Declination
Topographic maps indicate the declination of a map. Declination is the difference between true north (the actual northern-most point on the planet) and magnetic north (the site of a tremendous amount of magnetic rock. The needle of a compass points this direction).
e.g. In Ottawa, the declination value is 13 degrees.

## Slide 8: Declination

## Slide 9: Magnetic Declination

## Slide 10: Grids
There are four types of grids that we will explore in this course:
  Alphanumeric grid
  4-point grid
  6-point grid
  Latitude and Longitude

## Slide 11: Alphanumeric Grid
Uses letters and numbers to locate a general area.

## Slide 12: 4-Point Grid
A system of locating objects using two digits along each axis.
Vertical lines are measured first, and horizontal lines are measured second.
In this example, A is located in box:
B is located in box:
20 70
30 80

## Slide 13: How to work out 6 figure grid references…
Let us first look at how the 6 figure grid reference is made up.
Let us take 216 322 as an example.
The first 3 figures refer to the easting of the point (or the distance along the map)
While the second 3 figures refer to the northing of the point (or the distance up the map).

## Slide 14: Let us find the 6 figure grid reference for the church on the map below
The church is in grid square 22 31.
If we imagine that square divided into 10 parts, the church is 2 tenths further east and 2 tenths further north.
So the 6 figure grid reference will be 222 312

## Slide 15: Now try a few on your own…
What is the 6 figure grid reference for the church?
325 460

## Slide 16: Now try a few on your own…
What is the 6 figure grid reference for Lodge Farm?
306 454

## Slide 17: Now try a few on your own…
What is the 6 figure grid reference for the school?
323 465

## Slide 18: TO THE TEXT!!!
Find the 4-point and 6-point grid references for each of the letters located on the map on p.25.
Using the figures on p.34, list the grid references requested in Figures 3-3 and 3-4.
Complete questions 1-10 on p. 32.